## Slide 1
Sandbox Runtime Cost Analysis
Per-Pod Cost Comparison: kata-qemu vs kata-clh vs gVisor vs kata-fc (Firecracker)
AWS EKS · us-west-2 · On-Demand Pricing · April 2026
Pod Spec: 4 containers × stress-ng (gateway 150m/1G + config-watcher 100m/256M + envoy 100m/256M + wazuh 100m/512M) Total per pod: 450m CPU / 2048 MiB memory (Guaranteed QoS, request = limit) All scenarios: full CPU + memory stress, zero idle pods

## Slide 2
Per-Pod Monthly Cost — Lower is Better
Instance cost ÷ max stable pods = cost per sandbox instance per month
m7g.2x gVisor+EFS
$17.02/mo
14 pods · m7g.2xlarge
m7g.metal kata-fc
$21.18/mo
90 pods · m7g.metal
m8i.2x gVisor
$22.08/mo
14 pods · m8i.2xlarge
m8i.2x kata-clh
$23.78/mo
13 pods · m8i.2xlarge
c7g.metal kata-fc
$30.79/mo
55 pods · c7g.metal
m8i.2x kata-qemu
$44.15/mo
7 pods · m8i.2xlarge
m7g.metal FC+EBS PVC
$68.08/mo
28 pods · m7g.metal
Note: On-Demand pricing, us-west-2. RI/Savings Plans can reduce by 30-60%. Graviton instances are ~23% cheaper than Intel equivalents.

## Slide 3
Full Comparison Matrix
场景 | 实例 | 架构 | vCPU/RAM | 运行时 | Max Pods | 理论值 | 瓶颈 | $/Pod/hr | $/Pod/月
m8i.2x kata-qemu | m8i.2xlarge | Intel x86 | 8v / 32G | kata-qemu | 7 | 12 | VM crash (restart) | $0.0605 | $44.15
m8i.2x kata-clh | m8i.2xlarge | Intel x86 | 8v / 32G | kata-clh | 13 | 13 | 调度器内存上限 | $0.0326 | $23.78
m8i.2x gVisor | m8i.2xlarge | Intel x86 | 8v / 32G | gVisor | 14 | 14 | 调度器内存上限 | $0.0302 | $22.08
m7g.2x gVisor+EFS | m7g.2xlarge | Graviton | 8v / 32G | gVisor | 14 | 14 | 调度器内存上限 | $0.0233 | $17.02
m7g.metal kata-fc | m7g.metal | Graviton | 64v / 256G | kata-fc | 90 | 91 | CPU 99% | $0.0290 | $21.18
c7g.metal kata-fc | c7g.metal | Graviton | 64v / 128G | kata-fc | 55 | 55 | 内存 99% | $0.0422 | $30.79
m7g.metal FC+EBS PVC | m7g.metal | Graviton | 64v / 256G | kata-fc | 28 | 28 | EBS 挂载上限 (31 shared) | $0.0933 | $68.08
测试参数: 每 Pod 4 容器 (gateway 150m/1G + config-watcher 100m/256M + envoy 100m/256M + wazuh 100m/512M), Guaranteed QoS, stress-ng full load (CPU 95% + vm-keep) Pod Overhead: kata-qemu 100m/250Mi · kata-clh 100m/200Mi · kata-fc 250m/130Mi · gVisor 无 定价: AWS On-Demand, us-west-2, 730 hrs/month

## Slide 4
Same Instance, Different Runtimes — m8i.2xlarge (8 vCPU, 32 GiB)
kata-qemu
嵌套 VM
7
stable pods
$44.15
per pod / month
理论达成: 58%
瓶颈: VM crash (restart)
kata-clh
嵌套 VM
13
stable pods
$23.78
per pod / month
理论达成: 100%
瓶颈: 调度器内存上限
gVisor
用户态内核
14
stable pods
$22.08
per pod / month
理论达成: 100%
瓶颈: 调度器内存上限
💡 同一台 m8i.2xlarge: kata-qemu 每 Pod $44/月 → kata-clh $24/月 (↓46%) → gVisor $22/月 (↓50%)
Note: gVisor 安全隔离等级低于 Kata VM 隔离, syscall 兼容性有限制, EFS I/O 不可用

## Slide 5
Bare Metal Scaling: kata-fc (Firecracker) on Graviton
裸金属 = 无嵌套虚拟化开销, Firecracker microVM 直接运行在硬件上
m7g.metal
64 vCPU · 256 GiB · Graviton
90
stable pods (0 restarts)
$21.18/pod/月
实例 $2.6112/hr
瓶颈: CPU 99%
c7g.metal
64 vCPU · 128 GiB · Graviton
55
stable pods (0 restarts)
$30.79/pod/月
实例 $2.3200/hr
瓶颈: 内存 99%
m7g.metal + EBS PVC
64 vCPU · 256 GiB · Graviton
28
stable pods (0 restarts)
$68.08/pod/月
实例 $2.6112/hr
瓶颈: EBS 挂载上限 (31 shared)
💡 m7g.metal 90 pods = $21/pod/月 — 比嵌套虚拟化 kata-qemu 便宜 52%
⚠️ 挂 EBS PVC 后仅 28 pods (EBS 共享槽位限制 31), 成本升至 $68/pod/月 — 比无 PVC 贵 3.2x
Note: kata-fc 需要 devmapper thinpool, busybox 单层镜像限制, 不支持 CPU hotplug (aarch64)

## Slide 6
Key Takeaways
🏆
最低成本 (VM 隔离)
m7g.metal + kata-fc: $21/pod/月 (90 pods)
裸金属消除嵌套虚拟化开销, Firecracker 轻量 microVM, Graviton 价格优势
💰
最低成本 (用户态隔离)
m7g.2x + gVisor: $17/pod/月 (14 pods)
零 overhead, 100% 调度器理论达成, Graviton 比 Intel 便宜 23%
⚠️
kata-qemu 最贵
m8i.2x + kata-qemu: $44/pod/月 (仅 7 pods)
QEMU VMExit 开销大, 嵌套虚拟化下仅达 58% 理论密度, VM crash
📦
EBS PVC 是隐藏瓶颈
m7g.metal + EBS PVC: 仅 28 pods ($68/pod/月)
Nitro 共享槽位 31 = EBS + ENI, 扣除 root/devmapper/ENI 后仅 28 PVC 可用
🔄
运行时选择影响 2-4x 成本
同一实例, 不同运行时: $22 vs $44/pod/月
kata-clh 比 kata-qemu 便宜 46% (同一台 m8i.2xlarge)
Data source: kata-benchmark-v2 stress tests, April 2026 · Pricing: AWS On-Demand us-west-2